## Slide 1: How the 128 stations were chosen, and IMD data limits
Replaces the 'challenges' box on slide 2. The six Undecided stations stay in the zone table; they are a zoning question, not a data gap.
Basis of selection (449 station codes → 128 used)
Test | Rule | Result
Complete day | All 8 three-hourly readings present | 85.8% of station-days
Usable season | 1 Mar–31 Oct: ≥90% complete days, no gap >15 days | Counted per year, 2016–25
Tier | Usable seasons of 10: A 8–10 · B 5–7 · C 1–4 · D 0 | A 43 · B 56 · C 29 used; D 321 dropped
Monthly coverage | ≥28 usable days in every calendar month over 10 years | All 128 pass (with spline)
Zone tag | ECBC 2017 list · NBC 2016 regional rule · project precedent · undecided | 43 · 78 · 1 · 6
Same rule as the earlier notebook: all 449 stations reproduce the same tier.
Data challenges in the IMD record
Only 8 readings a day. No hourly record; the true daily peak can fall between the 14:30 and 17:30 IST readings.
Most stations unusable. 321 of 449 station codes (71%) have no usable cooling season in 2016–2025.
Gaps inside the 128. 14.2% of station-days are incomplete: 4.5% fillable (1–2 readings), 2.7% 9-hour gaps, 7.0% three or more missing.
Uneven coverage. Warm-Humid has 59 stations; Temperate 2 and Cold 3. 29 stations are Tier C.
Cleaning needed. 4,209 blank rows, repeated readings and impossible dates removed (5.31 M rows → 5.305 M valid readings).
No zone in IMD metadata. Each station was placed using ECBC 2017 or NBC 2016.
Notes: Source: methodology note sections 'Source data' and 'Which stations are used'. Station-day split is for the 128 stations, 434,165 station-days.

## Slide 2: Method: how 3-hourly IMD readings become hours in each bin
What we do
Method A, no spline: each IMD reading counts for 3 hours. Nothing is filled in.
Method B, spline: a smooth daily curve through the 8 readings gives 24 hourly values. Days missing 1–2 non-adjacent readings are filled from that day's own curve.
Tested: hiding one real reading and predicting it gave the lowest error of 5 methods (0.94 °C) and almost no bias at 14:30 IST.
Outcome
IMD takes a reading at 14:30 IST, close to the hottest time of day, so the hot-hour bins rest on real measurements. The spline only fills the hours between readings.
Who else builds bin-hour tables, and how
Method | Same as ours | Different
India, BEE Sch. 19 / IS 1391 (in force) | 1 °C bins from 24 °C; whole-year hours (5,774 → 1,600) | One typical year per city (ISHRAE 2014, 54 cities); one national table; stops at 43 °C
ISO 16358-1 (Malaysia, Thailand, Indonesia, Philippines, Vietnam) | Same bin-hour formula ISEER uses | Fixed reference table, 21–35 °C, 1,817 h; Malaysia uses it unchanged, not local data
Saudi Arabia, SASO 2663:2021 | National weather data replaces ISO default bins; covers very hot hours | One national table
China, GB 21455 | 1 °C bins starting at 24 °C | Top bin 38 °C (2013 edition); one national table
US Engineering Weather Data (AFM 88-29) | 3-hourly readings counted as 3 hours each, as in our Method A | No interpolation; 5 °F bins
No other scheme we found builds zone-wise tables from a 10-year raw station record; most use one national table or typical-year files.
Notes: Sources: BEE Schedule 19 (2015) Table 1; ISO 16358-1:2013; Energy Commission Malaysia (Suruhanjaya Tenaga) Guide on MEPS for AC (2021): bins per ISO 16358-1 Table 3; LBNL/U4E ASEAN AC harmonization report (2021); SASO 2663:2021; GB 21455-2013/2019; AFM 88-29 Engineering Weather Data (1978). Verify the GB and SASO bin ranges against the standard text before external use.

## Slide 3: Hours per year in each zone, compared with the table in force
Each figure = hours in ONE typical year at ONE station, averaged over the zone's stations. Built from 10 years of IMD readings (2016–2025); not a 10-year total. Whole year, with spline.
Zone | Stations | All hours ≥24 °C | vs 5,774 | Hours ≥35 °C | 43–44 °C | 44 °C and above | 43 °C and above (new)
Composite | 42 | 5,598 | −3% | 692 | 15.4 | 12.2 | 27.6
Hot-Dry | 16 | 6,222 | +8% | 1,019 | 20.8 | 26.0 | 46.8
Warm-Humid | 59 | 7,226 | +25% | 256 | 0.7 | 0.3 | 1.0
Temperate | 2 | 5,465 | −5% | 144 | 0.0 | 0.0 | 0.0
Cold | 3 | 1,615 | −72% | 33 | 0.0 | 0.0 | 0.0
Undecided | 6 | 6,379 | +10% | 696 | 7.0 | 2.6 | 9.6
Table in force (BEE Sch. 19) | 54 cities | 5,774 | — | ≈642 | ≈11 (43 bin) | not counted | ≈11
Reading the table: a Hot-Dry station has about 47 hours a year at 43 °C or above, four times the ≈11 hours in the table in force. Cooling-months (Mar–Oct) figures for 43 °C and above are identical, since all such hours fall in those months.
≈ BEE per-bin annual hours derived as bin hours × 5,774/1,600 (e.g. 43 °C: 3 × 3.609 ≈ 11). Replace with the exact Schedule 19 Table 1 column before circulation.

## Slide 4: Hours at 44 °C and above: results under each option
Hours per year per station, zone average (whole year, with spline). Bracket: the same hours on BEE's 1,600-hour scale; the table in force puts 3 of 1,600 hours in its 43 °C bin.
Zone | Data today: 43–44 °C ¦ 44 °C+ | Option A: keep 24–43 °C, drop 44 °C+ | Option B: top bin = 43 °C and above | Option C: add a separate 44 °C+ bin
Hot-Dry | 20.8 ¦ 26.0 | 43 bin 20.8 (5.3) 26.0 h lost | 43+ bin 46.8 (12.0) +125% | 43 bin 20.8 (5.3) 44+ bin 26.0 (6.7)
Composite | 15.4 ¦ 12.2 | 43 bin 15.4 (4.4) 12.2 h lost | 43+ bin 27.6 (7.9) +79% | 43 bin 15.4 (4.4) 44+ bin 12.2 (3.5)
Undecided | 7.0 ¦ 2.6 | 43 bin 7.0 (1.8) 2.6 h lost | 43+ bin 9.6 (2.4) +37% | 43 bin 7.0 (1.8) 44+ bin 2.6 (0.7)
Warm-Humid | 0.7 ¦ 0.3 | 43 bin 0.7 (0.2) | 43+ bin 1.0 (0.2) | 44+ bin 0.3 (0.1)
Temperate, Cold | 0 ¦ 0 | No change | No change | No change
Option A
Same table shape as today, but undercounts the hottest hours where ACs work hardest (26 h/yr lost in Hot-Dry).
Option B
Keeps 20 bins and the ISEER formula; the top bin in Hot-Dry grows from 5.3 to 12.0 of 1,600 hours, 4× the 3 in force.
Option C
Most precise, but adds a 21st bin and a change to the ISEER calculation and the IS 1391 / IS 18154 table.
Notes: Bracketed values = zone hours scaled to 1,600 using that zone's own total hours ≥24 °C (e.g. Hot-Dry 46.8/6,222 × 1,600 = 12.0). If the deck's options are labelled differently, map them to: A = cap at 43 and drop, B = merge into top bin, C = new 44+ bin.

## Slide 5: Assumptions and next steps
Assumptions behind the numbers
1. Smooth daily curve. Temperature between IMD's 3-hourly readings follows a smooth daily cycle (spline tested: 0.94 °C mean error, no bias at 14:30).
2. Recent decade = today's climate. 2016–2025 represents current conditions; no adjustment for the warming trend, which would add hot hours.
3. Missing days look like recorded days. A station's missing days in a month are assumed similar to its recorded days in that month.
4. Stations stand for their zone. Each station counts equally in its zone average; no weighting by population or AC stock.
5. Station air = air at the AC. Airport and observatory readings represent outdoor-unit air; urban heat and rooftop effects are not captured.
Next steps
Expert consultation on the method (BEE, BIS, ISHRAE, IMD): spline or not, bin labels, months, the 44 °C option and zone weighting.
Fill the data gaps: request IMD hourly AWS data and daily maximum temperatures for weak stations; cross-check with hourly airport (METAR) records.
Where we need more readings | Why
Temperate zone | Only 2 stations: Bengaluru (Tier C) and Coimbatore (zone not on ECBC list)
Cold zone | 3 stations (Srinagar, Sundernagar, Shillong); none from Ladakh, Uttarakhand hills or Sikkim
Hot-Dry, Tier C | Ajmer, Aurangabad, Deesa, Solapur, Udaipur: this zone sets the 43 °C+ hours
Central India heat belt | Delhi (Palam), Gwalior, Jabalpur, Raipur, Bhopal: large markets, Tier C
Deccan, Undecided | Gulbarga, Anantapur (Tier C): more stations needed to settle the zone

## Slide 6: Annex: first result against the table in force (5,774 hours)
Rough comparison, whole year, with spline. Hours per year per station, zone average. A national table still needs a zone-weighting decision.
Zone | Hours ≥24 °C | vs 5,774 | Hours ≥35 °C | vs ≈642 | Share ≥35 °C
Composite (42) | 5,598 | −3% | 692 | +8% | 12.4%
Hot-Dry (16) | 6,222 | +8% | 1,019 | +59% | 16.4%
Warm-Humid (59) | 7,226 | +25% | 256 | −60% | 3.5%
Temperate (2) | 5,465 | −5% | 144 | −78% | 2.6%
Cold (3) | 1,615 | −72% | 33 | −95% | 2.1%
Undecided (6) | 6,379 | +10% | 696 | +8% | 10.9%
All 128, simple mean* | 6,368 | +10% | 508 | −21% | 8.0%
Table in force | 5,774 | — | ≈642 | — | 11.1%
* Each of the 128 stations counted once. Not a national weighting: 59 of 128 stations are Warm-Humid, which pulls total hours up and hot hours down.
Chart: Hours at 35 °C and above, per year
| Cold | Temperate | Warm-Humid | BEE table (in force) | Composite | Undecided | Hot-Dry
Hours ≥35 °C per year | 33 | 144 | 256 | 642 | 692 | 696 | 1019
Takeaway: totals are within 8% of 5,774 in Composite and Hot-Dry, but the hot tail is heavier in Hot-Dry. Which zones carry how much weight decides the national table.
Notes: Per-bin version (24 to 43 and 44+, 10-year counted hours by zone) to follow once IMD_BinHours_by_Zone_2_WITH_SPLINE.xlsx is available in this workspace. BEE ≥35 °C annual hours derived as 178 of 1,600 bin hours × 5,774/1,600 = 642.